## Slide 1: STRIVE COMPILER BINDING
Directorate of Computer architecture & Engineering

## Slide 2: Objective
“To Bind a PC to a Microcontroller in such a way that only a registered user is able to program it”

## Slide 3: Justification
An attacker can erase a microcontroller program on a PCB and install a malicious program on it
This can compromise the mission and no trace would be found of who programmed it
Solution:
Since we have the control of chip manufacturing, we can implement a mechanism in the hardware which would not allow any program to run on it unless it is compiled by our own compiler

## Slide 4
Novel Key Sharing Mechanism
Debug unit accessibility controlled via key verification
Hardware Security Features
Processor locked to a specific PC for execution
Enhanced protection against unauthorized code execution by a custom instruction
NECOP Secure Compiler

## Slide 5
Core
Debug Unit
Flash Memory
Custom Instruction
Authenticator
Architecture
Security
Flash memory that stores the keys is not connected to the system bus. It is only accessible by a compare unit which is triggered by a custom instruction
Debug is only enabled when the Authenticator allows it to
Authenticator needs the last key in order to access the flash memory.
compare
uart
uart
PC

## Slide 6
Flash memory
My custom Key
Start
Key-2
Key-3
Enable
End
compare
Key-1
Debug Unit
Code Block
My custom instruction
opcode
Imm Value
compare
Code main
Imm value
Compiler Binding
Key-1

## Slide 7: Key Binding
Key Generation
A 26-bit key is generated dynamically.
Components: Timestamp, Machine ID, UUID, Random Selection.
Database Management
A centralized database stores key bindings.
Enables tracking of secure execution and maintains integrity.
Log Tracking
The system can retrieve the last log entry for security purposes.

## Slide 8: Custom Instruction
Instruction Details
Kc is successfully added as first class instruction in RISCV ISA so It can be used in C/assembler programs and supported by GCC + binutils
Name kc
Syntax Kc rd imm20
Format I-Type
Encoding Imm[20 bits] rd[5]

## Slide 9: Testing my GCC
Windows Executable
Addition of Instruction

## Slide 10: Testing my code with custom GCC

## Slide 11: GUI

## Slide 12: Application Features

## Slide 13: Code Compiling

## Slide 14: Hex Viewer

## Slide 15: Key Matching

## Slide 16: Updated Hex

## Slide 17: Connect Button

## Slide 18: Program Button